## Slide 1
Chapter 18
Introduction to
Network
Layer
Copyright © The McGraw-Hill Companies, Inc. Permission required for reproduction or display.

## Slide 2
    18-1 NETWORK-LAYER SERVICES
Before discussing the network layer in the Internet today, let’s briefly discuss the network-layer services that, in general, are expected from a network-layer protocol. Figure 18.1 shows the communication between Alice and Bob at the network layer. This is the same scenario we used in Chapters 3 and 9 to show the communication at the physical and the data-link layers, respectively.

## Slide 3
Figure 18.1: Communication at the network layer

## Slide 4
18.18.1 Packetizing
The first duty of the network layer is definitely packetizing: encapsulating the payload in a network-layer packet at the source and decapsulating the payload from the network-layer packet at the destination. In other words, one duty of the network layer is to carry a payload from the source to the destination without changing it or using it. The network layer is doing the service of a carrier such as the postal office, which is responsible for delivery of packages from a sender to a receiver without changing or using the contents.

## Slide 5
18.18.2 Routing and Forwarding
Other duties of the network layer, which are as important as the first, are routing and forwarding, which are directly related to each other.

## Slide 6: Routing
Network is a combination of LANs and WANs connected via Routers.
More than one route from source to destination.
Finding the best route.
Coordinate knowledge about neighbors.
Come up with consistent tables that are used when packets arrive.
Routing protocols are: Routing Information Protocol (RIP) Interior Gateway Protocol (IGRP) Open Shortest Path First (OSPF) Exterior Gateway Protocol (EGP) Enhanced Interior Gateway Routing Protocol (EIGRP)

## Slide 7: Forwarding
Routing is applying strategies and running some protocols to create the decision-making tables for each router.
Forwarding can be defined as the actions applied by router when a packet arrives at its interface.
Tables are called forwarding tables or Routing tables.
Use information in the packet header to find corresponding output interface using the tables.

## Slide 8
Figure 18.2: Forwarding process

## Slide 9
18.18.3 Other Services
Let us briefly discuss other services expected from the network layer.

## Slide 10
Error Control
Can be implemented but usually ignored.
Inefficient due to fragmentation of packets at routers.
Checksum is there to check header.
Whole datagram is not checked.
ICMP provides error control if datagrams are discarded or if there is some unknown information in the header.

## Slide 11
Flow Control
Does not directly provide any flow control.
Reasons are:
  Job at receiver is simple so rare chances of overwhelming.
  Transport layer have buffers to control flow.
  Another level of flow control adds complications
  System becomes less efficient.
Notes: Security Protocol is IPSec.

## Slide 12
    18-2 PACKET SWITCHING
From the discussion of routing and forwarding in the previous section, we infer that a kind of switching occurs at the network layer. A router, in fact, is a switch that creates a connection between an input port and an output port (or a set of output ports), just as an electrical switch connects the input to the output to let electricity flow.

## Slide 13
Packet Switching
Two Switching Techniques:
  Circuit Switching(Use at Physical layers)
  Packet Switching(Network Layer)
Source and Destination sends and receives packets one by one.
Destination waits for all the packets of the same message to arrive before sending it to Transport Layer.
Two approaches to route packets:
  Datagram Approach
  Virtual Circuit Approach
Notes: Security Protocol is IPSec.

## Slide 14
18.2.1 Datagram Approach
When the Internet started, to make it simple, the network layer was designed to provide a connectionless service in which the network-layer protocol treats each packet independently, with each packet having no relationship to any other packet. The idea was that the network layer is only responsible for delivery of packets from the source to the destination. In this approach, the packets in a message may or may not travel the same path to their destination. Figure 18.3 shows the idea..
Notes: The switches in this type of network are called Routers.
Each packet independent entity. No relationship between packets belonging to the same message.

## Slide 15: Datagram Approach- Connectionless Service
The switches in this type of network are called Routers.
Each packet independent entity. No relationship between packets belonging to the same message.
Packet is routed on the basis of source and destination information in the header.
Forwarding is based on destination address.

## Slide 16
Figure 18.3: A connectionless packet-switched network

## Slide 17
Figure 18.4: Forwarding process in a router when used in a
connectionless network

## Slide 18
18.2.2 Virtual-Circuit Approach
In a connection-oriented service (also called virtual-circuit approach), there is a relationship between all packets belonging to a message. Before all datagrams in a message can be sent, a virtual connection should be set up to define the path for the datagrams. After connection setup, the datagrams can all follow the same path. In this type of service, not only must the packet contain the source and destination addresses, it must also contain a flow label, a virtual circuit identifier that defines the virtual path the packet should follow.

## Slide 19
18.2.2 Virtual-Circuit Approach
To Create a connection-Oriented Service a three phase process is used:
Set up
Data Transfer
Tear Down
Set Up Phase: Source and Destination addresses are used to make table entries for the connection oriented service.
Tear Down Phase: Source and Destination inform the router to delete corresponding entries.

## Slide 20
Figure 18.5: A virtual-circuit packet-switched network

## Slide 21
Figure 18.6: Forwarding process in a router when used in a virtual
circuit network

## Slide 22
Figure 18.7: Sending request packet in a virtual-circuit network
Notes: Request and Ack packets sent during setup phase

## Slide 23
Figure 18.8: Sending acknowledgments in a virtual-circuit network

## Slide 24
Figure 18.9: Flow of one packet in an established virtual circuit

## Slide 25
    18-3 NETWORK-LAYER PERFORMANCE
The upper-layer protocols that use the service of the network layer expect to receive an ideal service, but the network layer is not perfect. The performance of a network can be measured in terms of delay, throughput, and packet loss. Congestion control is an issue that can improve the performance.

## Slide 26
18.3.1 Delay
All of us expect instantaneous response from a network, but a packet, from its source to its destination, encounters delays. The delays in a network can be divided into four types: transmission delay, propagation delay, processing delay, and queuing delay. Let us first discuss each of these delay types and then show how to calculate a packet delay from the source to the destination..

## Slide 27
18.3.2 Throughput
Throughput at any point in a network is defined as the number of bits passing through the point in a second, which is actually the transmission rate of data at that point. In a path from source to destination, a packet may pass through several links (networks), each with a different transmission rate. How, then, can we determine the throughput of the whole path? To see the situation, assume that we have three links, each with a different transmission rate, as shown in Figure 18.10.

## Slide 28
Figure 18.10: Throughput in a path with three links in a series

## Slide 29
Figure 18.11: A path through the Internet backbone

## Slide 30
Figure 18.12: Effect of throughput in shared links

## Slide 31
18.3.3 Packet Loss
Another issue that severely affects the performance of communication is the number of packets lost during transmission. When a router receives a packet while processing another packet, the received packet needs to be stored in the input buffer waiting for its turn. A router, however, has an input buffer with a limited size. A time may come when the buffer is full and the next packet needs to be dropped. The effect of packet loss on the Internet network layer is that the packet needs to be resent, which in turn may create overflow and cause more packet loss.

## Slide 32
18.3.4 Congestion Control
Congestion control is a mechanism for improving performance. In Chapter 23, we will discuss congestion at the transport layer. Although congestion at the network layer is not explicitly addressed in the Internet model, the study of congestion at this layer may help us to better understand the cause of congestion at the transport layer and find possible remedies to be used at the network layer. Congestion at the network layer is related to two issues, throughput and delay, which we discussed in the previous section.

## Slide 33
Figure 18.13. Packet delay and throughput as functions of load

## Slide 34
Figure 18.14: Backpressure method for alleviating congestion

## Slide 35
Figure 4.15: Choke packet

## Slide 36
    18-4 IPv4 ADDRESSES
The identifier used in the IP layer of the TCP/IP protocol suite to identify the connection of each device to the Internet is called the Internet address or IP address. An IPv4 address is a 32-bit address that uniquely and universally defines the connection of a host or a router to the Internet. The IP address is the address of the connection, not the host or the router.

## Slide 37
18.4.1 Address Space
A protocol like IPv4 that defines addresses has an address space. An address space is the total number of addresses used by the protocol. If a protocol uses b bits to define an address, the address space is 2b because each bit can have two different values (0 or 1). IPv4 uses 32-bit addresses, which means that the address space is 232 or 4,294,967,296 (more than four billion). If there were no restrictions, more than 4 billion devices could be connected to the Internet.

## Slide 38
Figure 18.16: Three different notations in IPv4 addressing

## Slide 39
Figure 18.17: Hierarchy in addressing

## Slide 40
18.4.2 Classful Addressing
When the Internet started, an IPv4 address was designed with a fixed-length prefix, but to accommodate both small and large networks, three fixed-length prefixes were designed instead of one (n = 8, n = 16, and n = 24). The whole address space was divided into five classes (class A, B, C, D, and E), as shown in Figure 18.18. This scheme is referred to as classful addressing. Although classful addressing belongs to the past, it helps us to understand classless addressing, discussed later.

## Slide 41
Figure 18.18: Occupation of the address space in classful addressing
Notes: Subnets supernets, Address Depletion

## Slide 42
18.4.3 Classless Addressing
With the growth of the Internet, it was clear that a larger address space was needed as a long-term solution. The larger address space, however, requires that the length of IP addresses also be increased, which means the format of the IP packets needs to be changed. Although the long-range solution has already been devised and is called IPv6, a short-term solution was also devised to use the same address space but to change the distribution of addresses to provide a fair share to each organization. The short-term solution still uses IPv4 addresses, but it is called classless addressing.
Notes: 1990s ISPs introduced
ISP: provide internet services but does not create an internet site

## Slide 43
Figure 18.19: Variable-length blocks in classless addressing

## Slide 44
Figure 18.20: Slash notation (CIDR)
Notes: Slash Notation or Classless InterDomain Routing CIDR

## Slide 45
Figure 18.21: Information extraction in classless addressing
Set all suffix bits
to 1s
Set all suffix bits
to 0s
Notes: Address Mask

## Slide 46
A classless address is given as 167.199.170.82/27. We can find the above three pieces of information as follows. The number of addresses in the network is 232− n = 25 = 32 addresses. The first address can be found by keeping the first 27 bits and changing the rest of the bits to 0s.
Example 18.1
The last address can be found by keeping the first 27 bits and changing the rest of the bits to 1s.
18.46

## Slide 47
We repeat Example 18.1 using the mask. The mask in dotted-decimal notation is 256.256.256.224 The AND, OR, and NOT operations can be applied to individual bytes using calculators and applets at the book website.
Example 18.2
18.47
Notes: Network Address
Helps in Routing and forwarding

## Slide 48
In classless addressing, an address cannot per se define the block the address belongs to. For example, the address 230.8.24.56 can belong to many blocks. Some of them are shown below with the value of the prefix associated with that block.
Example 18.3
18.48

## Slide 49
Figure 18.22: Network address
Notes: Network Addresses

## Slide 50
An ISP has requested a block of 1000 addresses. Since 1000 is not a power of 2, 1024 addresses are granted. The prefix length is calculated as n = 32 − log21024 = 22. An available block, 18.14.12.0/22, is granted to the ISP. It can be seen that the first address in decimal is 302,910,464, which is divisible by 1024.
Example 18.4
18.50

## Slide 51
An organization is granted a block of addresses with the beginning address 14.24.74.0/24. The organization needs to have 3 subblocks of addresses to use in its three subnets: one subblock of 10 addresses, one subblock of 60 addresses, and one subblock of 120 addresses. Design the subblocks.
Example 18.5
Solution
There are 232– 24 = 256 addresses in this block. The first address is 14.24.74.0/24; the last address is 14.24.74.255/24. To satisfy the third requirement, we assign addresses to subblocks, starting with the largest and ending with the smallest one.
18.51

## Slide 52
a. The number of addresses in the largest subblock, which requires 120 addresses, is not a power of 2. We allocate 128 addresses. The subnet mask for this subnet can be found as n1 = 32 − log2 128 = 25. The first address in this block is 14.24.74.0/25; the last address is 14.24.74.127/25.
b. The number of addresses in the second largest subblock, which requires 60 addresses, is not a power of 2 either. We allocate 64 addresses. The subnet mask for this subnet can be found as n2 = 32 − log2 64 = 26. The first address in this block is 14.24.74.128/26; the last address is 14.24.74.191/26.
Example 18.5 (continued)
18.52

## Slide 53
c. The number of addresses in the largest subblock, which requires 10 addresses, is not a power of 2. We allocate 16 addresses. The subnet mask for this subnet can be found as n1 = 32 − log2 16 = 28. The first address in this block is 14.24.74.192/28; the last address is 14.24.74.207/28.
Example 18.5 (continued)
If we add all addresses in the previous subblocks, the result is 208 addresses, which means 48 addresses are left in reserve. The first address in this range is 14.24.74.208. The last address is 14.24.74.255. We don’t know about the prefix length yet. Figure 18.23 shows the configuration of blocks. We have shown the first address in each block.
18.53

## Slide 54
Figure 18.23: Solution to Example 4.5

## Slide 55
Figure 18.24 shows how four small blocks of addresses are assigned to four organizations by an ISP. The ISP combines these four blocks into one single block and advertises the larger block to the rest of the world. Any packet destined for this larger block should be sent to this ISP. It is the responsibility of the ISP to forward the packet to the appropriate organization. This is similar to routing we can find in a postal network. All packages coming from outside a country are sent first to the capital and then distributed to the corresponding destination.
Example 18.6
18.55

## Slide 56
Figure 18.24: Example of address aggregation
Notes: Subnets, Address Aggregation

## Slide 57: Special Addresses
This-host Address: (only address)0.0.0.0/32 host needs to send datagram but doesnot know its own address.
Limited-Broadcast Address: (only address) 255.255.255.255/32 Router or host needs to send a datagram to all devices in a network.
Loopback Address: 127.0.0.0/8(block) used for testing a piece of software in the machine.
Private Addresses: (4 Blocks) used in case of NAT. 10.0.0.0/8, 172.16.0.0/12, 192.168.0.0/16, 169.254.0.0/16
Multicast Addresses: 224.0.0.0/4(block) is reserved for multicast transmission.

## Slide 58
18.4.4 DHCP
After a block of addresses are assigned to an organization, the network administration can manually assign addresses to the individual hosts or routers. However, address assignment in an organization can be done automatically using the Dynamic Host Configuration Protocol (DHCP). DHCP is an application-layer program, using the client-server paradigm, that actually helps TCP/IP at the network layer.

## Slide 59
Figure 18.25: DHCP message format

## Slide 60
Figure 18.26: Option format

## Slide 61
Figure 18.27: Operation of DHCP

## Slide 62
Figure 18.28: FSM for the DHCP client

## Slide 63
18.4.5 NAT
In most situations, only a portion of computers in a small network need access to the Internet simultaneously. A technology that can provide the mapping between the private and universal addresses, and at the same time support virtual private networks, which we discuss in Chapter 32, is Network Address Translation (NAT). The technology allows a site to use a set of private addresses for internal communication and a set of global Internet
addresses (at least one) for communication with the rest of the world.
Notes: Limited number of IPs in IPv4
If the size of business increase, ISP will have to grant a new range of IP addresses as the addresses before or after the current range may not be free

## Slide 64
Figure 18.29: NAT
Notes: Incase of NAT communication must be initiated by the private IP host. POP command generated for email then the emails are retrieved

## Slide 65
Figure 18.30: Address translation
18.65
Notes: Drawbacks: one private address can communicate at a time. Solution: Pool of public IPs used Drawback: Limited number of hosts can be connected, one private host cant access two server program at a time Solution: use both IP addresses and port addresses

## Slide 66
Figure 18.31: Translation

## Slide 67
Table 18.1: Five-column translation table
18.67

## Slide 68
    18-5 FORWARDING OF IP PACKETS
We discussed the concept of forwarding at the network layer earlier in this chapter. In this section, we extend the concept to include the role of IP addresses in forwarding. As we discussed before, forwarding means to place the packet in its route to its destination.

## Slide 69
18.5.1 Destination Address Forwarding
We first discuss forwarding based on the destination address. This is a traditional approach, which is prevalent today. In this case, forwarding requires a host or a router to have a forwarding table. When a host has a packet to send or when a router has received a packet to be forwarded, it looks at this table to find the next hop to deliver the packet to.

## Slide 70
Figure 18.32: Simplified forwarding module in classless address

## Slide 71
The first address in a block is normally not assigned to any device; it is used as the network address that represents the organization to the rest of the world.
Note

## Slide 72
Configuration and addresses in a subnetted network

## Slide 73
Make a forwarding table for router R1 using the configuration in Figure 18.33.
Example 18.7
Solution
Table 18.2 shows the corresponding table.
Table 18.2: Forwarding table for router R1 in Figure 4.46
18.73

## Slide 74
Figure 18.33: Configuration for Example 4.7

## Slide 75
Instead of Table 18.2, we can use Table 18.3, in which the network address/mask is given in bits.
Example 18.8
Table 18.3: Forwarding table for router R1 using prefix bits
When a packet arrives whose leftmost 26 bits in the destination address match the bits in the first row, the packet is sent out from interface m2. And so on.
18.75

## Slide 76
Show the forwarding process if a packet arrives at R1 in Figure 18.33 with the destination address 180.70.65.140.
Example 18.9
Solution
The router performs the following steps:
18. The first mask (/26) is applied to the destination address. The result is 180.70.65.128, which does not match the corresponding network address.
2. The second mask (/25) is applied to the destination address. The result is 180.70.65.128, which matches the corresponding network address. The next-hop address and the interface number m0 are extracted for forwarding the packet (see Chapter 5).
18.76

## Slide 77
Figure 18.34: Address aggregation

## Slide 78
Figure 18.35: Longest mask matching

## Slide 79
As an example of hierarchical routing, let us consider Figure 18.36. A regional ISP is granted 16,384 addresses starting from 120.14.64.0. The regional ISP has decided to divide this block into 4 subblocks, each with 4096 addresses. Three of these subblocks are assigned to three local ISPs, the second subblock is reserved for future use. Note that the mask for each block is /20 because the original block with mask /18 is divided into 4 blocks.
Example 18.10
The figure also shows how local and small ISPs have assigned addresses.
18.79

## Slide 80
Figure 18.35: Hierarchical routing with ISPs